## Slide 1: A Fast Algorithm for Structured Low-Rank Matrix Recovery with Applications to Undersampled MRI Reconstruction
Greg Ongie*, Mathews Jacob
Computational Biomedical Imaging Group (CBIG)
University of Iowa, Iowa City, Iowa.
April 14, 2016
ISBI 2016, Prague

## Slide 2
Compressed Sensing MRI Reconstruction
smoothness/sparsity regularization penalty
recovery posed in discrete image domain
Example: TV-minimization
Rel. Error = 5%
25% k-space

## Slide 3
Drawbacks to TV Minimization
Discretization effects:
  Lose sparsity when discretizing to grid
Unable to exploit structured sparsity:
  Images have smooth, connected edges
Sensitive to k-space sampling pattern [Krahmer & Ward, 2014]

## Slide 4
Off-the-Grid alternative to TV [O. & Jacob, ISBI 2015], [O. & Jacob, SampTA 2015]
Continuous domain piecewise constant image model
Model edge set as zero-set of a 2-D band-limited function
“Finite-rate-of-innovation curve” [Pan et al., IEEE TIP 2014]
image
edge set

## Slide 5
2-D PWC functions satisfy an annihilation relation
spatial domain
Annihilation relation:
Fourier domain
multiplication
annihilating filter
convolution

## Slide 6
Matrix representation of annihilation
2-D convolution matrix
built from k-space samples
2(#shifts) x (filter size)
Cartesian
k-space samples
vector of filter coefficients
apply weights

## Slide 7
Matrix representation of annihilation
Basis of algorithms: Annihilation matrix is low-rank
Filter size: 33x25
rank 300
Ex: Shepp-Logan
k-space

## Slide 8
Pose recovery from missing k-space data as structured low-rank matrix completion problem

## Slide 9
Lift
Toeplitz
1-D Example:
Missing data
Pose recovery from missing k-space data as structured low-rank matrix completion problem

## Slide 10
Toeplitz
1-D Example:
Pose recovery from missing k-space data as structured low-rank matrix completion problem
Complete matrix
By minimizing rank

## Slide 11
Project
Toeplitz
1-D Example:
Pose recovery from missing k-space data as structured low-rank matrix completion problem
Complete matrix
By minimizing rank

## Slide 12
Fully sampled TV (SNR=17.8dB) Proposed (SNR=19.0dB)
50% k-space samples
(random uniform) error error
(Retrospective undersampled 4-coil data compressed to single virtual coil)

## Slide 13
SAKE [Shin et al., MRM 2014]
  Image model: Smooth coil sensitivity maps (parallel imaging)
LORAKS [Haldar, TMI 2014]
  Image model: Support limited & smooth phase
ALOHA [Jin et al., ISBI 2015]
  Image model: Transform sparse/Finite-rate-of-innovation
Off-the-grid models [O. & Jacob, ISBI 2015], [O. & Jacob, SampTA 2015]
undersampled k-space
recovered k-space
Structured Low-rank
Matrix
Recovery
Emerging Trend: Fourier domain low-rank priors for MRI reconstruction

## Slide 14
Main challenge: Computational complexity
Image: 256x256 Filter: 32x32
~106 x 1000
~108 x 105 Cannot Hold in Memory!
256x256x32
32x32x10
2-D
3-D

## Slide 15
Outline
Prior Art
Proposed Algorithm
Applications

## Slide 16
Cadzow methods/Alternating projections [“SAKE,” Shin et al., 2014], [“LORAKS,” Haldar, 2014]
No convex relaxations. Use rank estimate.

## Slide 17
Cadzow methods/Alternating projections [“SAKE,” Shin et al., 2014], [“LORAKS,” Haldar, 2014]
Project onto space of rank r matrices -Compute truncated SVD:
Project onto space of structured matrices
  -Average along “diagonals”
Alternating projection algorithm (Cadzow)

## Slide 18
Drawbacks
Highly non-convex
Need estimate of rank bound r
Complexity grows with r
Naïve approach needs to store large matrix
Cadzow methods/Alternating projections [“SAKE,” Shin et al., 2014], [“LORAKS,” Haldar, 2014]

## Slide 19
Nuclear norm minimization
Singular value thresholding step -compute full SVD of X!
Solve linear least squares problem -analytic solution or CG solve
ADMM = Singular value thresholding (SVT)

## Slide 20
“U,V factorization trick”
Low-rank factors
Nuclear norm minimization

## Slide 21
Nuclear norm minimization with U,V factorization [O.& Jacob, SampTA 2015], [“ALOHA”, Jin et al., ISBI 2015]
Singular value thresholding step -compute full SVD of X! SVD-free  fast matrix inversion steps
Solve linear least squares problem -analytic solution or CG solve
UV factorization approach

## Slide 22
Drawbacks
Big memory footprint—not feasible for 3-D
U,V trick is non-convex
Nuclear norm minimization with U,V factorization [O.& Jacob, SampTA 2015], [“ALOHA”, Jin et al., ISBI 2015]

## Slide 23
None of current approaches exploit structure of matrix liftings (e.g. Hankel/Toeplitz)
Can we exploit this structure to give a more efficient algorithm?

## Slide 24
Outline
Prior Art
Proposed Algorithm
Applications

## Slide 25
IRLS: Iterative Reweighted Least Squares
Proposed for low-rank matrix completion in [Fornasier, Rauhut, & Ward, 2011], [Mohan & Fazel, 2012]
Solves:
Idea:
Proposed Approach: Adapt IRLS algorithm for nuclear norm minimization
Alternate

## Slide 26
Original IRLS: To recover low-rank matrix X, iterate

## Slide 27
Original IRLS: To recover low-rank matrix X, iterate
We adapt to structured case:

## Slide 28
Original IRLS: To recover low-rank matrix X, iterate
We adapt to structured case:
Without modification, this approach is still slow!

## Slide 29
Idea 1: Embed Toeplitz lifting in circulant matrix
Toeplitz
Circulant
*Fast matrix-vector products with by FFTs

## Slide 30
Idea 2: Approximate the matrix lifting
*Fast computation of by FFTs
Pad with extra rows

## Slide 31
Build Gram matrix with two FFTs—no matrix product
Computational cost: One eigen-decomposition of small Gram matrix
eig( )
Explicit form:
svd( )
Simplifications: Weight matrix update

## Slide 32
Convolution with single filter
Simplifications: Least squares subproblem
Fast solution by CG iterations
Sum-of-squares average:

## Slide 33
Proposed GIRAF algorithm
Update annihilating filter -Small eigen-decomposition
Least-squares annihilation
  -Solve with CG
GIRAF algorithm
GIRAF = Generic Iterative Reweighted Annihilating Filter
Adapt IRLS algorithm +simplifications based on structure

## Slide 35
GIRAF complexity similar to iterative reweighted TV minimization
IRLS TV-minimization
GIRAF algorithm
Local update:
Least-squares
problem
Global update:
Least-squares
problem
w/small SVD
Edge weights
Image
Image
Edge weights

## Slide 36
Table: iterations/CPU time to reach convergence tolerance of NMSE < 10-4.
Convergence speed of GIRAF
Scaling with filter size
CS-recovery from 50% random k-space samples
Image size: 256x256 Filter size: 15x15
(C-LORAKS spatial sparsity penalty)
CS-recovery from 50% random k-space samples
Image size: 256x256 (gradient sparsity penalty)

## Slide 37
Outline
Prior Art
Proposed Algorithm
Applications

## Slide 38
GIRAF enables larger filter sizes  improved compressed sensing recovery
+1 dB improvement

## Slide 39
GIRAF enables extensions to multi-dimensional imaging: Dynamic MRI
GIRAF
Fourier sparsity
TV
error images
Fully sampled
[Balachandrasekaran, O., & Jacob, Submitted to ICIP 2016]

## Slide 40
Correction of ghosting artifacts
In DWI using annihilating filter framework and GIRAF
[Mani et al., ISMRM 2016]
GIRAF enables extensions to multi-dimensional imaging: Diffusion Weighted Imaging

## Slide 41
Summary
Emerging trend: Powerful Fourier domain low-rank penalties for MRI reconstruction
  State-of-the-art, but computational challenging
  Current algs. work directly with big “lifted” matrices
New GIRAF algorithm for structured low-rank matrix formulations in MRI
  Solves “lifted” problem in “unlifted” domain
  No need to create and store large matrices
Improves recovery & enables new applications
  Larger filter sizes  improved CS recovery
  Multi-dimensional imaging (DMRI, DWI, MRSI)

## Slide 42
References
Krahmer, F., & Ward, R. (2014) Stable and robust sampling strategies for compressive imaging. Image Processing, IEEE Transactions on, 23(2): 612-622.
Pan, H., Blu, T., & Dragotti, P. L. (2014). Sampling curves with finite rate of innovation. Signal Processing, IEEE Transactions on, 62(2), 458-471.
Shin, P. J., Larson, P. E., Ohliger, M. A., Elad, M., Pauly, J. M., Vigneron, D. B., & Lustig, M. (2014). Calibrationless parallel imaging reconstruction based on structured low‐rank matrix completion. Magnetic resonance in medicine, 72(4), 959-970.
Haldar, J. P. (2014). Low-Rank Modeling of Local-Space Neighborhoods (LORAKS) for Constrained MRI. Medical Imaging, IEEE Transactions on, 33(3), 668-681
Jin, K. H., Lee, D., & Ye, J. C. (2015, April). A novel k-space annihilating filter method for unification between compressed sensing and parallel MRI. In Biomedical Imaging (ISBI), 2015 IEEE 12th International Symposium on (pp. 327-330). IEEE.
Ongie, G., & Jacob, M. (2015). Super-resolution MRI Using Finite Rate of Innovation Curves. Proceedings of ISBI 2015, New York, NY.
Ongie, G. & Jacob, M. (2015). Recovery of Piecewise Smooth Images from Few Fourier Samples. Proceedings of SampTA 2015, Washington D.C.
Ongie, G. & Jacob, M. (2015). Off-the-grid Recovery of Piecewise Constant Images from Few Fourier Samples. Arxiv.org preprint.
Fornasier, M., Rauhut, H., & Ward, R. (2011). Low-rank matrix recovery via iteratively reweighted least squares minimization. SIAM Journal on Optimization, 21(4), 1614-1640.
Mohan, K, and Maryam F. (2012). Iterative reweighted algorithms for matrix rank minimization." The Journal of Machine Learning Research 13.1 3441-3473.
Acknowledgements
Supported by grants: NSF CCF-0844812, NSF CCF-1116067, NIH 1R21HL109710-01A1, ACS RSG-11-267-01-CCE, and ONR-N000141310202.

## Slide 43
Thank you! Questions?
Exploit convolution structure to simplify IRLS algorithm
Do not need to explicitly form large lifted matrix
Solves problem in original domain
GIRAF algorithm for structured low-rank matrix recovery formulations in MRI